## Slide 1: Solar Energy Harvesting Device
For Xylem Water Meter
EE494

## Slide 2: PRESENTORS
Siddhant Khera –– Report Compilation and Electrical Design Development & Production, General Management
Serena LaFave –– Report Writing, Soldering and Prototyping
Krystal Bakr –– Managing Technical Documentation, Project Financials and Research

## Slide 3: Today’s Agenda
Executive Summary
Why Solar?
Conceptual Model: Initial to Final
Components: Solar & Battery
Final Schematic Custom PCB Design
Drawbacks of Current Design
Enclosure Details
Bill of Material
Note on Ethics
Conclusion & Future Work

## Slide 4: Executive Summary
An energy harvesting system for a Xylem water meter, using Li-ion and Solar
Designed a custom PCB, measures only 33mm x 22mm
Battery storage provided for up to 37 days at 5mW peak power
Max dimensions 84mm x 59mm x 33mm, under the 100mm x 100mm x 60mm requirement
Manufactured BOM at $2.92, under $3 target set by Xylem
Environmental and other factors considered, Ethical sourcing most important
  Unable to meet Ethical sourcing requirement due to cost
  Environmentally: recyclable material used, up to 60% parts fully recyclable

## Slide 5: Energy Harvesting Technology
Options include:
Thermoelectric
Solar
Hydroelectric

## Slide 6: Thermoelectric
Works from a temperature difference [1]
At least 40°C difference needed [1]
Same ambient temperature
Battery heat
Fig 1: Thermoelectric Generator [2]
Notes: 40 deg diff: http://vi.raptor.ebaydesc.com/ws/eBayISAPI.dll?ViewItemDescV4&item=152641213248&category=181723&pm=1&ds=0&t=1555920406000&ver=0
pic: https://www.makerlab-electronics.com/product/thermoelectric-power-generator-module-teg-sp1848-27145/

## Slide 7: Hydroelectric
Difficult installation
Maintenance
Fig 2: In-Pipe Hydroelectric System [3]
Notes: pic https://reprogrammingthecity.com/generating-power-from-city-water-infrastructure/

## Slide 8: Solar
Readily available
  Small size
  Inexpensive
Yuma, Arizona: A very sunny place!
Fig 3: Solar Panel [4]
Notes: pic https://www.aliexpress.com/item/32827162063.html

## Slide 9
Yuma, Arizona
Fig 4: DNI Map of the US [5]
Fig 5: DNI Map of Arizona [5]
Notes: pic https://maps.nrel.gov/nsrdb-viewer/?aL=0&bL=clight&cE=0&lR=0&mC=4.740675384778373%2C22.8515625&zL=2

## Slide 10: Conceptual Model: Initial
In the preliminary stages of our project, we designed a conceptual model that represented the basic concept of what we believed our design should do in order to accomplish the main goal of harvesting energy for the water meter.
5V to 5.5V Solar panel
Charge Controller
3.7V Li-Ion Battery
Water meter
Fig 6: Initial Conceptual Model [8]

## Slide 11: Conceptual Model: Final
Fig 7: Final Conceptual Model [8]

## Slide 12: What did we change?
Added a DC-DC boost converter
  Change in charge controllers
    MCP → TP4056
Temperature control
  NTC thermistor, new feature given our new charge controller
  Low temperature protections
Battery Protection
  DW01A chip
    Adds overcharging, over discharging, and overcurrent protection to the battery
Notes: Section 6.5.5 from Final Report

## Slide 13: Components
Fundamental Components:
Battery
Solar panel

## Slide 14: Components: Battery
Battery Technology: Lithium-ion
Standardized voltage that fit out needs
High charge cycle and energy density
No memory effect
Readily available in standard sizes, low cost
Table 1: Battery Technologies [8]

## Slide 15: Components: Battery
Battery size
Calculations show that 454 mAh of battery storage = 14 days
Fig 8: Battery Calculation Result [8]

## Slide 16: Components: Battery
Tie between Unbranded and Kanavano
Tiebreaker: Cost
Table 2: Battery Decision Matrix [8]

## Slide 17: Components: Battery
1200mAh = Up to 37 days
Only $0.62
Fig 9: Final Battery Choice [9]
Notes: battery pic: https://www.aliexpress.com/item/32893018458.html?spm=a2g0o.cart.0.0.50683c001kuDRz&mp=1

## Slide 18: Components: Solar Panel
Original solar panel (Interim Design Report): 5V, 60mA
  Designed the circuit around these values
Size
Table 3: Solar Panel Decision Matrix [8]

## Slide 19: Components: Solar Panel
Final choice: Yucosolar
5.5V, 70mA
0.385W
~3.12h to fill battery
$0.73/unit
Fig 10: Yucosolar Panel [10]
Notes: solar panel: https://www.aliexpress.com/item/33009866599.html?spm=a2g0o.productlist.0.0.2b1f6593YIFY2Q&algo_pvid=9768576c-2208-451a-8873-919287d6f879&algo_expid=9768576c-2208-451a-8873-919287d6f879-6&btsid=0be3764315892259202404537e31a7&ws_ab_test=searchweb0_0,searchweb201602_,searchweb201603_

## Slide 20: Final schematic
Uses MT3086 (DC-DC Boost converter), TP4056 (Li-ion Charging Chip), DW01 (Li-ion battery protection)
Motivation to use MT3068 was to circumvent the low voltage issue from solar panel
Solar panel minimum under non-bright situations in 2.3V
MT3608: DC-DC Boost converter, Input required 2V, output constant 4.5V
TP4056: Min VCC = 4.0V, input is output from MT3608, connects to DW01
DW01: protects battery from overcharge, overdischarge and short-circuit etc
Used iterative design process, isolated circuit before bringing it all together

## Slide 21: Chip Details
TP4056
  Constant current voltage linear charger
  Min VCC = 4.0V, input is output from MT3608, connects to DW01
  Temperature sensing using NTC Thermistor
DW01
  Protection IC for One-Cell Lithium-Ion
    Paired with 8205 dual n-channel MOSFET for logic
  Protects from Overcharge, Overdischarge, Short Circuit
MT3608
  Boosts DC voltage to min VCC of TP4056
  Input required 2V, output constant 4.5V
NTC Thermistor
  Temperature sensitive resistor, known resistance at various temperatures
  Pin 1 of TP4056 checks if Vsupply is between 45% to 80%
  Designed voltage divider, using NTC Thermistor, at 45% value at 0ºC, 80% at 45ºC

## Slide 22
Fig 11: Final Li-ion Charging Circuit [10]

## Slide 23: Printed Circuit Board (PCB)
Allows for small size in the enclosure
Single PCB instead of multiple ones
Drives down manufacturing cost
Trace width = 25mm, allows for testing up to 1A
Hardest: Placing components to manage traces and routing
Costs $0.03 to manufacture, $0.18 with assembly for manufacturer (could be cheaper)
Fig 13: 3D View of PCB [10]
Fig 12: Photo View of PCB [10]

## Slide 24: Drawbacks of current design
Lacks reverse polarity protection
Load cannot be connected with the battery simultaneously

## Slide 25: Enclosure
Goals:
IP64 or greater
  Dust-tight
  Waterproof –– Splashed water from any angle [11]
≤ $1
Made for outdoor use
  UV radiation
  Heat
  Impacts
Project Requirements
≤ 100mm x 60mm x 60 mm
-40 ºC to 85 ºC
Notes: IP rating: http://www.dsmt.com/resources/ip-rating-chart/

## Slide 26: Enclosure
Table 4: Enclosure Decision Matrix [8]

## Slide 27: Enclosure
Final Choice: Hongfa
84 x 59 x 33 mm
Made for outdoor use
ABS plastic, white
  Recyclable [13]
IP65
$0.90 + negotiable shipping
Fig 14: Closed view [8]
Fig 15: Open view [8]
Notes: enclosure photos: https://www.alibaba.com/product-detail/ABS-Outdoor-plastic-electronic-enclosure-waterproof_60667174101.html
abs is recyclable: https://www.plasticsinsight.com/resin-intelligence/resin-prices/abs-plastic/

## Slide 28: Enclosure
Cost improvement!
Contacted seller
Four 1.8mm holes
$0.558
FOB: free on board
Fig 16: Seller profile
Fig 17: Message from seller

## Slide 29: Enclosure
How to mount the solar panel?
Custom High Density Polyethylene (HDPE) holders
2 x 4mm screws
Use sealant to water and dust proof holes (see our Final Report for more details)
Fig 18: Mounted solar panel on enclosure lid (right) [8]
Fig 19: Holders

## Slide 30: Enclosure
Mounting internal components
PCB and battery holder
HDPE mounting plate
  $0.0075/unit [8]
2 x 4 mm screws
Fig 20: Mounting plate - holes:
Battery holder
Battery leads
PCB
All other holes: mount plate to enclosure [8]

## Slide 31: Final Enclosure
Fig 21: View of internal mounted components [8]

## Slide 32: Bill of Materials
Overall our BOM in total came out to $2.92, which was better than Xylem’s requirement of maximum $3 for high-volume production of the circuit and enclosure.
Used wholesale companies in order to purchase our components
  AliExpress
  LCSC Electronics
  Alibaba
  JCL PCB
Cheapest components to mention
  DW01A (Battery Protection IC): $0.029 for 10,000+ units (LCSC Electronics)
Most expensive component:
  Enclosure: $0.558 for 1000+ units
    Shipping is negotiable in bulk orders (A plus)
In order to stay below the $3 threshold we made many changes and compromises
  Change in suppliers

## Slide 33: Ethical Engineering
Is the topic: Ethics, subjective?
Least-cost or most humane design?
Are we exploiting Humans to enrich other Humans’ lives?
Child labor? Forced Labor? Mistreatment of Laborers?
Where do we draw the Moral line?

## Slide 34: Conclusions
Through teamwork, research, and perseverance we were able to meet and exceed the design requirements for the energy harvester. We were able to design a system using an alternative energy source - solar that will give power to a water meter. In our system we included
Protections against temperatures and for our battery
  Ensures the health and safety of the consumers
Our design is also
  Environmentally friendly
  Has manufacturability - can be reproduced on larger scales
So, what can we improve in the future?

## Slide 35: Future work
Improved Enclosure
  Using aluminum instead of plastic
      Can add heat sinks to the sides
        Helps cool down the battery
      Note: Aluminum is usually more expensive than plastic
        Would require more time customizing an aluminum enclosure and heat sinks that fit in our budget
Physically Produced Prototype
  Beneficial in allowing us to test in different weather conditions
  Propose a functioning prototype that can be used for commercial purposes

## Slide 36: Future work
Obtaining SPICE for Simulation
  Without SPICE libraries we were unable to prove our design worked at all
    In the future we would need access to these libraries to simulate
Sourcing Design from Nations with Effective Labor Laws
  Most of our project was sourced in China
    With more time, and in the future we would look into sourcing from other nations with strict labor laws
    Uphold ethics as engineers

## Slide 37: References
[1] S. unielec, “Thermoelectric Power Generator Ultra Thermal Conductive,” March 2020. [Online]. Available: https://www.ebay.com/ itm/1pcs-Thermoelectric-Power-Generator-Ultra-Thermal-Conductive-TEG-27145-/152641213248
[2] “BUHUSHUI 5V 25MA Mini Solar Panels.” Aliexpress.com, www.aliexpress.com/item/32827162063.html.
[3] NSRDB Data Viewer, National Renewable Energy Laboratory, maps.nrel.gov/nsrdb-viewer/?aL=0&bL=clight&cE=0&lR=0&mC=4.740675384778373%2C22.8515625&zL=2.
[4] Scottburnham. “Renewable Energy Under City Streets: Generating Power from City Water Pipes.” REPROGRAMMING THE CITY, 29 June 2019, reprogrammingthecity.com/generating-power-from-city-water-infrastructure/.
[5] “Thermoelectric Power Generator TEG Module SP1848-27145 Philippines - Makerlab Electronics.” Makerlab Electronics, www.makerlab-electronics.com/product/thermoelectric-power-generator-module-teg-sp1848-27145/.
[6] Cloudfront.net, “TP4056 1A Standalone Linear Li-lon Battery Charger with Thermal Regulation in SOP-8,” March 2020. [Online]. Available: https://dlnmh9ip6v2uc.cloudfront. net/datasheets/Prototyping/TP4056.pdf

## Slide 38: References
[7] Microchip, “MCP73831 Datasheet –– Miniature Single-Cell, Fully Integrated Li- Ion, Li-Polymer Charge Management Controllers,” January 2020. [Online]. Available: http://ww1.microchip.com/downloads/en/DeviceDoc/20001984g.pdf
[8] S. Khera, S. LaFave, K. Bakr, “EE494: Final Design Review,” The State University of New York, University at Buffalo, Spring 2020. [Online]. Available: https://www.ublearns.blackboard.com
[9] www.aliexpress.com, “Wholesale price 18650 battery 3.7V li-ion rechargeable battery 1200mah 1500mah 1800mah 2000mah 2200mah 2600mah,” May 2020. [Online]. Available: https://www.aliexpress.com/item/32893018458.html
[10] www.aliexpress.com, “Solar Cell 5.5V Mini Solar System 70mA,” May 2020. [Online]. Available: https://www.aliexpress.com/item/33009866599.html
[11] www.iprating.com, “ IP Rating Chart: Learn what IP means and what rating is best for your application” May 2020. [Online]. Available:http://www.dsmt.com/resources/ip-rating-chart/
[12] www.alibaba.com, “ABS Outdoor plastic electronic enclosure waterproof IP65 junction box” May 2020. [Online]. Available: https://www.alibaba.com/product-detail/ABS-Outdoor-plastic-electronic-enclosure-waterproof_60667174101.html
[13] www.plasticsinsight.com, “ABS Plastic Production, Price and Market Demand,” May 2020. [Online]. Available: https://www.plasticsinsight.com/resin-intelligence/resin-prices/ abs-plastic/